## Slide 1
Electrical Energy and Current

## Slide 2
Electrical Energy and Current
Electric Charge and Electric Current
An electric charge (q) exists if there is an excess or deficiency in the number of electrons. Mathematically, the number of electric charge, q, contained in a body is given by this equation:
q = ne
where q is the amount of charge, n is the number of electrons, and e is the charge of an electron. The unit for electric charge is coulomb (C).
On the other hand, the electric current (I), or the rate flow of charge, is caused by a stream of electrons moving from the negative voltage terminal toward the positive terminal. In general, it is defined as the number of coulombs of electric charge (Δq) that passes a cross section of a material divided by the time (Δt) required for the charge to pass. Thus:

## Slide 3
Electrical Energy and Current
The unit of measurement for current is the ampere (A). One ampere is equal to one coulomb of charge passing a point in a circuit in one second (1 A = 1 C/s.)
Remember that one coulomb is a lot of charge (1°C = 6 × 1018 electrons) and an electron has a charge of 1.6 × 10−19 C.
Example:
A long wire is connected to the terminals of a battery. In 8 seconds, 9.6 × 1020 electrons pass across a section along the wire. Calculate the current in the wire.
Given: t = 8 seconds, n = 9.6 × 1020 electrons
Find: I = ?

## Slide 4
Electrical Energy and Current
Solution:
Since the given value is the number of electrons, calculate first the electric charge. Use the calculated value of the electric charge to determine the electric current in the wire.

## Slide 5
Electrical Energy and Current
Ohm’s Law
experimented many substances to study electrical resistance.
He analyzed the various types of wires in order to determine the characteristics that affect the wire’s resistance.
Georg Simon Ohm
Quantities | Units | Descriptions
Current (I) | ampere (A) | rate flow of charge
Voltage (V) | volt (V) | measure of energy available to produce a flow of charges through a circuit
Resistance (R) | ohm (Ω) | amount of opposition to current flow within the material

## Slide 6
Electrical Energy and Current
One way of stating this relation is as follows: the voltage across any part of a circuit is proportional to the product of the current through that part of the circuit and the resistance of that part of the circuit. Stated as formula, the foregoing relationship is expressed as:
V = IR
Ohm’s law can also be used to find the value of the current , the value of the resistance ,and, as you will see after these examples, the power in the circuit.
Example:
What will be the current through a resistance of 150-Ω if the applied voltage across the
resistance is 117-V?
Given: V = 117 V, R = 150 Ω
Find: I = ?
Solution:
The current passing through a 150-Ω resistance with a voltage of 117 V is 0.78 A.

## Slide 7
Electrical Energy and Current
Electrical Power and Electrical Energy
The relationship stated by Ohm’s law can be used to calculate the electrical energy and electrical power. Electrical energy is expended at a rate of 1 W/s (or Joule, J). For every watt per second, 1 V causes a current of 1 A to flow. In this case, we say that the electrical power represented when 1 V causes 1 A to flow is 1 W. The relation is expressed as:
P = VI
where P is the electrical power, V is the voltage, and I is the electric current. Using Ohm’s law, we can substitute V = IR in the equation. Thus, it follows:
P = (IR) I = I2R

## Slide 8
Electrical Energy and Current
This equation is useful when the current and resistance are known. Similarly, by substituting the value V/R for I in the equation, we find that:
P= I2 R
Also, when V/R is substituted to I in P = VI, it follows:

## Slide 9
Electrical Energy and Current
The amount of electrical power can also determine the amount of electrical energy consumed in a given time interval. The consumer of electrical energy pays for the amount of energy used by one’s electrical equipment. This is measured by an instrument known as watt- hour or kilowatt-hour meter.
Electrical energy is sold per kilowatt-hour (kWh). One watt-hour of energy is consumed when 1 watt of power continues in action for 1 hour. Similarly, 1 kWh is consumed when the power is 1,000 W and the action of energy continues for 1 h or when a 100-W rate persists for 10 h. Thus, the amount of energy consumed is the product of the power and the time:
E = P × t = (IV) t
where E is the electrical energy, P is the electrical power, t is time, I is the electric current, and V is voltage.

## Slide 10
Electrical Energy and Current
Because all electrical equipment contain resistance, some heat always develops when current flows. Unless the equipment is to be used for producing heat, the heat due to the resistance of the equipment represents wasted energy. No electrical equipment or other machine is capable of converting energy received into useful work without some loss. The power that is furnished by a machine is called the machine’s input, and the power received from the machine is called its output. The efficiency of a machine is equal to the machine’s output divided by the machine’s input. That is:

## Slide 11
Electrical Energy and Current
The following examples will show you how to calculate the missing electrical quantities by using their identified relationship.
Examples:
1. The current through the starter motor of a car is 210 A. If the battery maintains 12 V across the motor, how much electric energy is delivered to the starter in 10.0 s?
Given: V = 12 V, I = 210 A, t = 10 s
Find: E = ?
Solution:
E = (P) t = (IV) t
E = (210 A) (12 V) 10 s = 2.5 × 104 J4 is the amount of electrical energy delivered to the starter motor of
the car.

## Slide 12
Electrical Energy and Current
2. A motor delivering 6.50 mechanical horsepower is drawing 26.5 A from a 220-V line. (a) How much electric power is the motor taking from the line? (b) What is the efficiency of the motor? (c) If power costs ₱8.50/kWh, how much does it cost to run the motor for 8 h?
Given: V = 220 V, I = 26.5 A, power rate = ₱8.50/kWh
Find: P, efficiency, and cost
Solution:
P = 6.5 hp = 6.5 hp × 746 (W/hp) = 4,850 W = 4.85 kW
a. The power taken by the motor is:
P = VI = 220 × 26.5 = 5,830 W = 5.83 kW
b. Efficiency = =0.832 83.2%
c. Because the motor consumes 5.83 kW in 8 h, the total consumption is 5.83 × 8 = 46.6 kWh. At ₱8.50/kWh, the cost will be 46.6 × ₱8.50 = ₱396.60.

## Slide 13
Electrical Energy and Current
Directions: Saving electricity is important to help conserve our energy resources. In this activity, list down the appliances in your house that use a great amount of electricity. Calculate the electrical energy (in kWh) consumed by each appliance. Then, provide a brief interpretation of the results that you gathered.
Activity:
Name of Appliance | Electrical Power | Number of Hours Used | Electrical Energy Consumed